## Slide 1: Processor Assignment
COMS30046 - Advanced Computer Architecture
Jacob Daniel Halsey

## Slide 2: The Instruction Set
I have chosen to simulate (a subset) of the ARM Cortex-M0 Thumb instruction set.
I have implemented 41 of the 56 supported instructions.
Each instruction takes (roughly) the same number of cycles as it would on the Cortex-M0
In addition I have also repurposed the SVC (supervisor call) instruction as a means of communicating between the running program and the simulator:
  SVC #1 to exit (Exit code in R0)
  SVC #2 to print (Address in R0, length in R1)

## Slide 3: The Programs - Toolchain
The simulator can support any simple C program, by using:
By default GCC will attempt to link with the Newlib implementation of the C standard library.
sim.c contains implementations of a few system calls to enable newlib to function in this environment – including _exit(), _write(), and _sbrk() using a small statically allocated heap.
Newlib also initialises the stack pointer to the address of the _stack symbol, defined in the default linker script as 0x80000.
arm-none-eabi-gcc -mthumb -mcpu=cortex-m0 -ffreestanding sim.c example.c –o example.elf

## Slide 4: The Programs – Binaries & Memory
memory.rs simulates a 32-bit address space, made up of “pages” mapped to particular address ranges within that space.
I am using the rust-elf library to parse the ELF binary files.
At launch each of the PT_LOAD program headers in the ELF has its data loaded as a “page” into the virtual memory, along with its specified write flag. These will correspond to:
  The text and data segments (code & constants) as read only
  The static variables as read/write
An additional “page” is created for use as a stack (starting from the 0x80000 address to match Newlib).
I am using the capstone-rs library to decode the ARM instructions.

## Slide 5: Scalar Simulator
Fetch()
Decode()
(1 Station)
Execute()
next_instr_addr
Some(fetched_instruction)
Some(fetched_instruction)
1 decoded_instructions
1 decoded_instructions
1 Cycle
1 Cycle
X Cycles
Next address += length of fetched instruction
Executing a branch will cause the next address to be changed

## Slide 6: Pipelined Simulator
Fetch()
Decode()
(1 Station)
Execute()
next_instr_addr
fetched_instruction
station.instruction
1 Cycle
Next address += length of fetched instruction
Completing a branch will cause the next address to be changed, and clear fetched/decoded instructions
next_instr_addr
fetched_instruction
Next State
If present & space for a decoded instruction – else do nothing
If present – else do nothing
decoded_instructions
station.instruction
Only if instruction needs another cycle, otherwise empty if complete
station.instruction
If space for a fetched instruction – else do nothing
Current State
Flush()
Writeback results to registers

## Slide 7: Pipelined Simulator
The pipelined simulator runs the fetch, decode, and execute steps in parallel. The code actually runs them concurrently on multiple threads.
This is not actually faster in practice (overhead exceeds performance benefits!) but it does effectively demonstrate that the stages can indeed be executed in parallel.
The pipeline means that instructions can be speculatively fetched and decoded – I am using a static predictor of not taken for any branching instruction.
A not taken branch therefore requires only 1 cycle, and a taken requires 3 cycles due to flushing the pipeline (much like the actual Cortex-M0).

## Slide 8: Out of Order Simulator
Fetch()
Decode()
Station 1
Execute()
next_instr_addr
fetched_instruction
station.instruction
1 Cycle
Next address += length of fetched instruction
Completing a branch will cause the next address to be changed, and clear fetched/decoded instructions
next_instr_addr
fetched_instruction
Next State
If present & space for a decoded instruction – else do nothing
If present & all input registers are ready – else do nothing
decoded_instructions
station.instruction
Only if instruction needs another cycle, otherwise empty if complete
station.instruction
If space for a fetched instruction – else do nothing
Current State
Flush()
Station 2
Execute()
Station 3
Execute()
Station N
Execute()
(Foreach
station)
If there is a free station and there are no control hazards issue the instruction
Broadcast result registers to other stations
Writeback results to registers

## Slide 9: Out of Order Simulator
The out of order simulator uses Tomasulo’s algorithm to deal with hazards and implement register renaming.
Each input register is filled in as ready if it is already available, or pending if it is dependent on another station currently executing.
When an instruction completes executing, its outputs are written back to the registers, as well as broadcast so that any other stations with pending registers for this station may be resolved.
pub source_registers: HashMap<RegId, Register>, pub enum Register { Ready(u32), Pending(StationId, RegId), }

## Slide 10: Experiment 1